Virtual frame buffer and VSYNC

---
application
Vfb on
XDR
Vfb on
XDR
request from
application
Kernel
Every VSYNC, do;
 - notify VSYNC to application
 - DMA and FLIP request
FLIP
GPU
fb on
GPU
fb on
GPU
Timing chart
V field
FLIP
t
DMA
FLIP
FLIP req
Output
VSYNC to application
mmap
/dev/fb
DMA
DMA
[Speaker Notes: Fig 3-1. Virtual frame buffer and VSYNC]

---
GPU
vsync
Flip done
vsync
Flip done
DMA
FLIP
with
sync
t
hvc
hvc
irq
Kernel
blocking
FB 0
FLIP req.
FB 0
DMA is kicked, if the former FLIP has been done
single frame buffer is used from Xserver, ...
[Speaker Notes: Fig 3-2. Vfb behavior in the kernel]

---
vsync
Flip done
vsync
Flip done
Kernel
DMA
FLIP req.
FLIP
with
sync
t
IOCTL
IOCTL
IOCTL
IOCTL
IOCTL
FSEL
FSEL
blocking
User
WAITFORVSYNC
FB
0
FB
1
2nd frame buffer
1st frame buffer
SCREENINFO
screen size,
num of frame buffers
ON
OFF
stop flipping in the kernel
end of user application
WAITFORVSYNC
[Speaker Notes: Fig 3-3. ioctl usage from the user App.]

---
Overview of Linux Installation

---
Game Area
Linux Area
PS3
Select “Format utility” menu
Built-in HDD
[Speaker Notes: Fig 1-1. Create Disk partition for Linux]

---
Other OS Flash Area
Boot flag: 0(= Game OS)
0
Kboot for Distro-A
Memory card/Optical Disc
Distro-A Web Page
Kboot for Distro-A
Flash Rom
PS3
Kboot for Distro-A
Select “Install Other OS” menu
Download
Install
[Speaker Notes: Fig 1-2. Boot Loader download & install]

---
Reserved Area in PS3 System Flash Rom
Header
CELL OS Area
Boot flag could be change by user
Other OS Area
Boot Loader Area
Boot loader image could be installed by user
Detail of Format
The format could be change.
Please refer PS3 website,
for up to date information
        <---------------- 16 bytes ------------------->
  address segment
  ------- +===============================================+ ----
 0x000000 | “cell_ext_os_area" | 0
        +-----------+-----------+-----------+-----------+
 0x000010 | version | offset1 | offset2 | (reserved)|
        +===========+===========+===========+===========+
 0x000020 | ldr format| ldr size | |
        +-----------+-----------+ |
        | |
        : (reserved) :
        | |
        +-----------+-----------------------------------+ ----
 0x000200 | boot flag | (reserved) | 1
        +-----------+-----------------------------------+
 0x000210 | |
        | |
        : (ext params) :
        | |
        +===============================================+ -----
 0x000400 | | 2(offset1)
        : (Other OS area) : :
        | | :
        +===============================================+ -----
        | | offset2
        : (boot loader area) : :
        | 　　 　 | :
  ------- +===============================================+ -----
 0x400000 8192
User changeable
boot loader image
install
[Speaker Notes: Fig 1-3.Other OS Flash Area Details]

---
User can switch which system to be booted though by PS3 System menu.
Other OS Flash Area
1
Boot flag: 0 -> 1 (Other OS)
Kboot for Distro-A
Flash Rom
PS3
Select “Default System” menu and set to “Other OS”
[Speaker Notes: Fig 1-4. Change Default system]

---
Power on
N
PS3 Env
 boot flag = 1
Y
Load & exec boot loader
from boot loader area
kboot
in kboot
Initialize Hardware and
mount devices
N
 Time out or
RET
Y
N
 User inputs?
Exec default kernel
Y
Exec user specified kernel
[Speaker Notes: Fig 1-5. Boot Flow Chart with Kboot]

---
SPE Programming Environment Overview

---
SPE
PPE
PPE Application
SPE Application
libspe
vector math library
SIMD math library
Linux Kernel
newlib
SPUFS

---
System Overview

---
Platform
support
SPU
support
video
output
control
graphics
audio
network
storage
USB
X
libspe
utils
SPE
support
Video
Output
Control
FB
ALSA
TCP/IP
etc
disk
NETWORK
SCSI
VFB
audio
GbE
storage
USB
System Bus
virtualization
PPU
SPUs
Video
Output
Control
Graphics
Audio
GbE
ATA
USB
wifi
HDD/
BD
Mouse/
ＫＢＤ
Bluetooth
PPC64 infrastructure
Mouse/KBD
Bluetooth
PAD
HW
Hyper
visor
Linux kernel
function
USB mass
PS3 PF support
[Speaker Notes: Fig 4-1. Structure of Linux for PS3]

---
Copyright © 2007 Sony Computer Entertainment Inc.
Copyright © 2006,2007 Sony Corp.
Permission is granted to copy, distribute and/or modify this document under the terms of the GNU Free Documentation License, Version 1.2 or any later version published by the Free Software Foundation; with no Invariant Sections, no Front-Cover Texts, and no Back-Cover Texts. A copy of the license is included in the section entitled "GNU Free Documentation License".
DISCLAIMER OF WARRANTY
THIS DOCUMENT IS PROVIDED "AS IS," AND COPYRIGHT HOLDERS MAKE NO REPRESENTATIONS OR WARRANTIES, EXPRESS OR IMPLIED, INCLUDING, BUT NOT LIMITED TO, WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, NON-INFRINGEMENT, OR TITLE; THAT THE CONTENTS OF THE DOCUMENT ARE SUITABLE FOR ANY PURPOSE; NOR THAT THE IMPLEMENTATION OF SUCH CONTENTS WILL NOT INFRINGE ANY THIRD PARTY PATENTS, COPYRIGHTS, TRADEMARKS OR OTHER RIGHTS.
COPYRIGHT HOLDERS WILL NOT BE LIABLE FOR ANY DIRECT, INDIRECT, SPECIAL OR CONSEQUENTIAL DAMAGES ARISING OUT OF ANY USE OF THE DOCUMENT OR THE PERFORMANCE OR IMPLEMENTATION OF THE CONTENTS THEREOF.

---
xres - 2 * xoff (pixel)
mmap address
+ 0 (byte)
1st frame buffer
offset to
1st fb
byte to next line
xres * BPP (byte)
+ xres * yres * BPP
(byte)
2nd frame buffer
offset to
2nd fb
 yres - 2 * yoff
(pixel)
 yres - 2 * yoff
(pixel)
offset